## Slide 1: Nail that Rail!…all you need to know to to become an ‘approved assessor' for basic housing modifications
Presented by Angela Vanderpoel
Community Occupational Therapist
28.09.10
15.11.10
Notes: <number>

## Slide 2: Objective
To provide Occupational Therapists with the knowledge & confidence to become ‘approved assessors’ to carry out basic housing modifications.
Notes: <number>

## Slide 3: Overview:
Becoming an approved EMS assessor
Basic housing modifications
Clinical reasoning
Handrails
Threshold ramps
Internal doorway widening
Lever taps
Sketching
Notes: <number>
EMS = Equipment Modification Service

## Slide 4: How can I become an approved assessor?
EMS core module (online)
    ‘Making EMS Applications’
    ‘Role of the EMS assessor’
    Certificate
‘Application for Accreditation form’
    Housing (basic)
APC
Is it difficult? No! Especially if you are here today…
Notes: <number>
Role of the EMS assessor - To establish eligibility,funding criteria, essential need, cost effective solution, alternatives
- To assess person's needs; explain funding, process, timeframes; provide information; determine solution; application to Enable NZ; liase with Enable NZ, person & family, contractor; follow-up to ensure the solution meets needs; training in safe use of the modification

## Slide 5: What is a “basic” housing modification?
A modification which is:
  non-structural
  low cost
  requires minor works
  does not require a building consent
Notes: <number>

## Slide 6: Basic modifications include:
Handrails ( internal and/or external)
Threshold ramps (up to 450mm long)
Internal door widening (standard hinged doors with no electrical works)
Lever taps
providing…..
Notes: <number>
For all other modifications it is necessary to become credentialed as a Housing Modifications assessor.
This requires additional training.

## Slide 7: providing….
…. it is determined that the housing modifications are essential to enable the person to:
Move in and around their home
Return to, or remain in, their home
Be the main carer of a dependent person
Notes: <number>
Refer to core module for detailed explanations
Note: Shared Care. Where a person is living in two homes on a regular basis (usually 3-4 days per week in each home), they can be described as living in shared care. This may be where a child is living in the homes of separated parents, a foster care arrangement, or where an elderly relative lives with different family members who provide care. This does not include people living in residential care as their funding arrangement generally consists of full-time ongoing support. People living in shared care may need equipment to support the person & their caregivers in both homes. Equipment should always be considered before housing modifications in the second home. (This criteria is generally for children aged 15 years and under who live in a long-term shared care situation.)

## Slide 8: Exclusions
Cost less than $200 incl gst
Reimbursement of work completed
Short term needs
Social or personal health needs
ACC related need
Purpose built properties
Notes: <number>
Refer to core module
Purpose built properties incl rest homes, licence to occupy, properties where the housing is supposed to be suitable for needs of people intended for that residence

## Slide 9: Clinical reasoning
Why is a modification needed? Consider the
the person
the environment
before jumping to
the solution
Notes: <number>
  the person - physical , functional, cognitive, sensory, psychosocial, sociocultural factors
  the home environment - internal & external features
  clinical reasoning
  - Identify need- observe current function. What does the person need to be able to do to stay in their own home?
- Identify issues- what are the problems and risks?
- Consider long term need – anticipate future needs relating to growth, ageing, progressive deterioration, prognosis.
- Identify goals- what does the person want to be able to do? What is the priority? Expectations?
- Problem solve & Consider options
- restorative approach Consider the possibility of improvement (eg with rehab post CVA or recovery following surgery)
- change technique
- equipment solution (particularly for bathroom mods but also for minor access mods)
- any other alternatives eg move from this home to a residence which is more readily accessible
Consider what will happen if the modification isn’t done
  even if at this stage the identified issue is relating to one area only ie if internal mods are being proposed, check access is suitable for possible future modification and if access mods are being proposed check internal doorways & bathroom.
Steps – consider design (steep, narrow, spiral, oversized, non uniform, ? poorly designed which would make it difficult even for an able bodied person, compliance with NZS) and condition of steps (uneven, open, cracked, slippery = home owners responsibility to provide “normal “ safe environment eg repairs & maintenance such as waterblasting steps)
Bathroom –layout, facilities, limiting factors/hazards for rail installation

## Slide 10: HANDRAILS
Notes: <number>

## Slide 11: Indicators for rails
Increase functional ability
Independence
Safety - reduce falls risk & incidence
Increase confidence
Long term need
Assist carer to help person
Essential need - no other options
Notes: <number>

## Slide 12: Considerations for rails
When selecting & positioning a rail consider:
    Environment where it will be installed
    Intended purpose of the rail
    Functional capacity & needs of user
    Relevant standards & legislation
Notes: <number>

## Slide 13: Step & Stair terminology
Riser is the height
Tread is the depth
Nosing is the edge
…of the step
Pitchline follows
the angle of the steps
(“More Accessible Housing for Independent Living” Rod A. Hunter 1992)
Notes: <number>
Riser is the vertical bit between treads.
Tread (aka the going) is where you put your foot.
Nosing is a potential hazard if it protrudes too far
Pitchline is a line connecting the top edges of the steps (nosings) of all treads on a flight

## Slide 14: NZ standards for steps & stairs NZS 4121:2001
Riser & treads should be uniform
Total rise in one flight should be < 2500mm
Maximum rise of each step should be 180mm
Minimum tread of each step should be 310mm
Nosings should be rounded & <25mm
No open risers
Notes: <number>
NZS 4121: 2001 Design for Access & Mobility – Buildings & Associated Facilities “ applies in effect to all new buildings & existing buildings, other than private residential buildings,when they are altered or there is a change in use”. Knowledge of NZS and principles of good design allows therapists to identify whether a client’s difficulties may be due not only to disability but also in part to poor design.
Open risers can be visually distracting. Can also catch toes on underside of treads when ascending. Walking stick could slip through gap. Closed riser allows user to stabilise foot or walking aid against it when ascending.

## Slide 15: NZ standards for rails Rails shall be…
parallel to pitchline of steps
installed @ height 900mm - 1000mm
32- 45mm diameter
continuous grip
extend 300mm beyond top & bottom steps
( Adapted from NZS 4121: 2001 Design for Access & Mobility – Buildings & Associated Facilities)
Notes: <number>
Height of rail – from nosing of the tread to the top of the handrail, parallel to pitch line .
Note fpr Paeds - May need second rail at lower height of 665-700mm to suit child.
Diameter – 32mm NZS but often use 25mm for domestic use
Extend 300mm – at top of steps this usually includes up into a porch (ie not finishing rail on side of house directly at top of steps). At bottom of steps this means 300mm past the tread width of the bottom step (not 300mm past the beginning of the first step). In our clients homes this is not often followed. Sometimes the rail will need to finish at the immediate end of the steps to avoid encroaching on a narrow driveway.

## Slide 16: and:
have 50mm clear space between wall & outside of rail
have rounded profile
pass the load bearing test
New build
requirements
Notes: <number>
50mm gap to allow clear space for hand
Rounded – shape does make a difference to how “graspable” a rail is.
a grip of 270’ is most desirable.
Load bearing test – shall be securely fixed, rigid & able to support a weight of 110kg applied in any direction at any point. Construction of the rail, how it is joined together and the thickness of the tubing (diameter) helps determine the strength of the rail & how much force can be applied through it.
New build requires a rail beside any more than 2 steps
There are also regulations for homes built after 1992.

## Slide 17: What type of rail is best?
Standard rail
Materials
Finish
Diameter
Length
Clamp-on rails
Suction rails
Notes: <number>
Standard rail is designed to be permanently fixed at both ends to structures of the wall, making them strong enough to take person’s weight.
Materials –aluminium powder coated, stainless steel, galv pipe, timber or plastic modular. If using in wet area use materials that do not rust. Metal materials retain temperatures & may not be suitable in very hot or cold environments
Finish- smooth or knurled. Knurled provides a slip resistant finish- recommended for use in wet areas and will also create more friction between the hand & the rail requiring less strength to maintain a firm grip on the rail. Usually more expensive.
- a rail that contrasts in colour against wall surface may assist visually impaired
Diameter– 25mm or 32mm public buildings 32mm, domestic usually 25mm except for bannister rails beside stairs
Lengths – for straight rails the most common std lengths used are 230mm (9”), 300mm (12”), 450mm (18”), 600mm (24”), 760mm (30”), 900mm (36”), 1200mm (48”). Custom made any size is possible (but more expensive). See Rail Configuration handout courtesy of Superquip website
NOTE Lengths are measured to centres of the brackets.
Clamp-on rails –are attached to side of bath or to taps are not therefore “fixed”. These are considered equipment and not modifications. Must only be used with caution as the direction & amount of force applied to the rail may alter its stability.
Suction rails are not recommended – are mounted on wall but not fixed securely into wall framework. Dependent on suction strength which may be affected by type of wall surface and wetness/dryness of wall, condition of rubber (like a nonslip mat). May be useful for assessment purposes (to determine if person can use rail in a certain place) or for temporary use eg on holiday but under supervision only. Suction rails are not funded by MoH.

## Slide 18: Up, down or sideways?
Horizontal
Vertical
L shaped
Diagonal
Hinged
U shaped
Other
Notes: <number>
Rails should be positioned close enough to reach & high enough to provide support to gain the required momentum & stability.
The direction or orientation of the rail depends on how it is to be used:
Horizontal may be indicated for pushing up from or lowering down to a seated position ( eg from toilet), stabilising when standing (eg in shower) or assistsing with a sideways transfer (eg from wheelchair onto toilet)
Vertical to reach & pull up on to stand from a sitting position (eg beside toilet or on wall above bath to use with a bath board), to maintain a standing position (eg standing in shower) or to climb up a single step (eg doorstep)
Lshaped 90’ combines the horizontal & vertical grab rail allowing the person to push, pull or do a combination of both ( forearm is supported while pulling up). Most often used by toilet & commonly seen in public toilets.
Diagonal on an angle usually 45’ . Used to rise from or lower to sitting. Allows forearm support which may be helpful if have poor or painful grip. Most often used by toilet or above bath rim. Can be straight or L shaped.
Hinged can be folded up out of the way when not in use. Usually on open side of toilet where there is no wall
U shaped – mounted at open part of U. Most often used in shower cubicles where there is no suitable fixing for a standard rail. Brackets are fixed into studs or dwangs above the cubicle or fixed to a separate timber mounting the width of he shower cubicle above the top edge.
Other – can have corner shaped or configured with a slide shower rail to which the shower hose is attached (recommended in wet area showers – allows user to hold onto vertical part of slide shower)

## Slide 19: Getting it right
Needs of the individual
Standard reach
Comfortable forward reach
How to know it’s the best place
Notes: <number>
Needs of the individual ie How will the person use it? Consider
functional capacity (technique , independent or carer assisted )
body mechanics (UL strength & ROM; whether person has full use of both hands; ability to grasp, hold, release. Observe where person instinctively puts their hands.)
size (height and arm reach)
environment – all different although HNZ use a limited number of designs
intended purpose of rail. Ensure the user has the capability to use it the way it was designed to be used
safety – consider balance, cognition, vision
Standard reach ref Selwyn Goldsmith.
there are differences between men & women – average man has > forward reach than women in standing & sitting
allow for reduced reach with age. Over 60yrs (average) forward reach is < by 40mm compared to under 60yrs
over 60yrs female fwd reach is approx 470mm from chest below bust.
Comfortable forward reach is another 100mm from static reach. Therefore a vertical rail on wall to use to pull up from sitting is likely to be ideally situated at approx 570mm from chest for female over 60yrs.
If there’s a choice, what’s the best place? Optimal positioning: the person says “that feels good”
maximises grip strength with good circulation of rail with fingers
requires minimal effort & energy to use
allows the wrist to align with the forearm, minimising wrist deviation
encourages good body alignment in relation to the rail

## Slide 20: Fixing into studs & dwangs
Why do we need to know?
The stud is…
The dwang is…
Rails MUST be securely fixed
What is behind the wall?
Notes: <number>
Why do we need to know?
It is useful for the therapist to know where the studs & dwangs are likely to be so you can be knowledgable about options for rail placement. However try and locate fixing only if you feel confident to do so. Recommend spending half a day with an installer to pick up tips on how to find studs.
Studs – the stud is the vertical timber of the framework behind the wall.
- In older houses the stud is usually 18” in from corner, then 36” & so on at 18” intervals. It is 2” thick.
- In newer houses the stud is usually 600mm in from corner, then 1200mm & so on at intervals. It is 40mm thick.
- Can be used for vertical rails, horizontal rails (between 2 or more studs), diagonal rails (between 2 studs)
Dwangs – are the horizontal timbers of the framework behind walls. Also known as noggins, cross bearers
- In older houses the dwangs are 12”, 24”, 36” alternating between studs. The dwang at 48” (1220mm) from floor will be continuous.
- In newer houses 300mm, 600mm, 1200mm from floor and so on alternating between the studs.
- generally not in the right place for a horizontal rail as too low or too high.
- can sometimes use for a vertical rail (between 2 dwangs).
Rails must be securely fixed Remember the load bearing test!
What is behind the wall?? Is it timber framed with cavities in behind wall covering or is it solid brick/concrete?
- Are there any hazards behind the walls? Eg electricity, water pipes

## Slide 21: Hot tips for finding studs!
Measure in from corner in 18” intervals (or 600mm intervals in newer houses)
Knock & listen
Visual clues
Check fixtures in place
Other useful places where rails can be put
Notes: <number>
Hot tips for finding stud positions –
visual clues - nail heads, raised plaster patches, joints or cracks can sometimes be seen on wallboard, behind plastic joining strips of wet wall lining
check fixtures in place - remove soap holder, toilet roll holder to see if they are fixed into stud.
- look at wall in adjoining room to bathroom (if bathroom is lined with seratone) and locate studs from that side
- do not assume existing towel rails or toilet roll holders are secured into studs!
other useful places – solid walls
- framing around window & door frames and cupboards,( underneath window sill beside a bath can be useful)
- solid timber of splash boards above bath, on window sill or window frame itself
- in corners
Thanks to Barry Pearson for the benefit of his experience!

## Slide 22: Determine solution – external rails
Location
Position & height
Type & fixing
Length
Add-ons
Other requirements
Mock-up to check it will work
Notes: <number>
Location – Which entrance? (front/back/side) Which is the most commonly used entrance to where a vehicle can be parked? Which entrance has least number of steps? Are there any environmental features such as the slope of the land, adjoining paths which affects usage?
Position – unilateral or bilateral. Depends on functional ability & whether person has full capability of both hands or if needs to use two rails @ same time for balance. If unilateral LHS or RHS? If there is no reason why it should be one side or other then install on the side away from the door hinge. If bilateral needs to be 900mm apart to use both rails at the same time.
Height – std at 900mm FFL Note for Paeds - May need second rail at lower height of 665-700mm to suit child.
Type –material, finish, diameter, custom made galvanised pipe, std size rail or combination (eg grabrail on doorframe of doorstep with galv pipe beside steps). Fixing to wall or freestanding? Depends on presence of a wall and what the surface is (weatherboard, brick, concrete, cladding).
Length –measure total overall length (helpful for contractor when quoting as costs on price per metre). Is it practical to extend the rail 300mm past the top and bottom? Note:There is a limit of 5 metres for funding via Enable NZ
Add-ons such as white edging or change in surface texture on nose of step( 25-50mm deep) to identify edges of treads may be required for visual impairment .
Non slip surfacing may be needed but this is readily available commercially from companies such as Anti Slip Solutions NZ Ltd (www.posigrip.co.nz) - encourage clients to have this done themselves for added safety.
Other requirements– such as equipment to be used in conjunction with rails eg half step at doorstep
- internal rails as well as external rails.
Mock up – use unattached rail lengths, broom handle, tape measure, garden hosing to give person a visual idea of where the rail will be positioned. Show photos of installed rails so person has realistic expectations.
- check it will work/is compatable with walking aid eg if uses stick in RH and rail is on RHS can they use stick in LH when using rail? Is walker used? Easy steps or ramp may be more cost effective in the long term if mobility is likely to deteriorate.

## Slide 23: Funding considerations external rails
REMEMBER!
One entrance
One property
No fix-it jobs!
Notes: <number>
EMS funding : One entrance If there is already a suitable rail in place at one entrance then EMS funding will not be available for a rail at an alternative entrance, irrespective of who funded the rail that is already in place
One property only. Funding will not be approved at more than one property unless there are extenuating circumstances such as shared care or client had to move from property, not by choice. Always check whether client may have had previous funding for this modification at this address or at a previous address.
Does not cover rectification work – uneven or oversized steps or steps in poor repair (cracked, slippery) will likely be considered as being unsafe for the general population regardless of disability, & therefore funding will not be available. This will be considered rectification work & home owners responsibility
Photo – non EMS funded rail - A rail was not installed at the time of step construction in 2000 and had to be fitted retrospectively in 2008 to get a WCC code of compliance. Note rail is 900mm FFL & does extend beyond top & bottom steps but it does not have a rounded profile.

## Slide 24: Determine solution – toilet rails
  to assist with sit to stand …
  to maintain balance when sitting…
  to assist with side
  transfer…
Notes: <number>
To assist with sit to stand from toilet and vice versa a 300mm long rail, fixed vertically into stud 36” (900mm) in from corner with bottom of rail at 900mm FFL often suits. Is inexpensive and most commonly used in existing situations/minor mods which people are self funding. This is usually approx 300mm in front of toilet bowl and will most likely coincide with the 570mm from chest measurement discussed earlier. This positioning works ideally with houses where studs are at 18” intervals but may not be possible in a newer home where studs are 600mm as this is too close for user when sitting on toilet.
To maintain balance while wiping self and/or assist with sideways transfer onto toilet a 450mm long rail fixed horizontally at 700mm FFL may be helpful.
A 90’ rail with horizontal & vertical sections 450mm x 450mm is ideal & will suit studs at 18” intervals. This is more likely to be specified as part of a more major housing mod.
A hinged rail on open side of toilet may be helpful.
For ambulant people in narrow toilet room which cannot fit walker,may need to extend horizontal rail along length of room to doorway
Usually it is not necessary to have a knurled/non slip surface rail

## Slide 25: Determine solution- shower cubicle
to aid stepping over lip….
to balance when
standing…
HOWEVER …
Notes: <number>
For stepping over lip into shower cubicle a 300mm long rail fixed vertically to outside entry to shower (on wall or into wooden shower frame if applicable) often suits. Bottom of rail @ 900mm FFL.
For stepping over lip into shower cubicle & standing to shower a 300-450mm long rail fixed vertically on wall opposite shower door, with bottom of rail at 900mm, often suits. Stud is usually located in centre of this wall. A horizontal Or a rail ( length to suit shower box width) fixed horizontally across any internal wall of shower at 900mm FFL may suit
HOWEVER…
Placement options will be restricted with glass walled showers, water pipes behind walls.
Generally are unable to install rails on the same wall as shower fittings unless the rail extends from one corner of wall to the other corner
Plastic/acrylic shower cubicles – may be able to install rail but the cubicle often sits out too far from wall behind it. Can be overcome by using U shaped hanging rail fixed on bracket above the shower cubicle. Check length of U so the horizontal part is 900mm FFL & check stability of rail (a longer rail may need to be made more stable by using sucker feet between rail and wall).
Be aware of risk of cracking tiles if drilling into tiled walls
If door opening restricts ability to install rail on outside of shower, consider removal of door replaced with curtain
Knurled rails recommended for use in wet area of shower but will be more expensive

## Slide 26: Determine solution- bath rails
to aid stepping
over side of bath…
to use with shower
above bath….
to lower self into
bath or lift up from
base of bath…
Notes: <number>
For stepping over side of bath a 450mm long rail fixed vertically on wall outside bath approx 750mm out from corner with bottom of rail at 900mm FFL often suits. Top of rail will be at 1350mm FFL which is suitable for reaching from outside the bath to step in or from inside the bath to step out.
For standing up from bath board or tub transfer seat and/or standing under shower a 450mm long rail vertically on wall above bath often suits. Fixed vertically 18” (450mm) or 36” (900mm) in from tap end corner(depending on how rail is to be used). Bottom of rail approx 750mm from base of bath . Using a 450mm long rail, the top of the rail will be 1200mm from the base of the bath which is suitable for reaching from outside of bath & from inside bath.
For lowering self into bath or lifting self up from seated position in base of bath a 450mm- 600mm long rail fixed horizontally or diagonally 100mm from top of bath rim is recommended. Approx 450mm in from tap end of bath

## Slide 27: All internal rails:
Consider other requirements
Mock-up to check it will work
Ensure expectations are realistic
$$$
Notes: <number>
Other requirements such as equipment to be used in conjunction with rails eg bath board, RTS
-external rails as well as internal rails
Mock up –hold sample rails in position to give person an idea of how the rail will look and what it will feel like to use it.
- show photos of other similar jobs
- attach self adhesive coloured dots to mark the position (also guides installer as to ideal position).
Funding – no funding via EMS for <$200 .
- encourage self responsibility (with information on “how to” – using info sheets available from this DHB). Advise of time frames if appln is made for MoH funding.

## Slide 28: THRESHOLD RAMPS
Notes: <number>

## Slide 29: Threshold ramps
Wedge shaped ramp
Gradient 1 in 8
Length 450mm max
Suits one low step at entry way
On outside or inside of door (or both)
( Adapted from NZS 4121: 2001 Design for Access & Mobility – Buildings & Associated Facilities)
Notes: <number>

## Slide 30: What are NZ standards for thresholds?
When the change in level at a stepped threshold is 20mm or less, no ramp is required
If the change in level is greater than 20mm a ramp is required which shall have a gradient not steeper than 1 in 8 & a length of no more than 450mm
Notes: <number>
If length is longer than 450mm it is considered a ramp not a threshold ramp

## Slide 31: Indicators for threshold ramps
Wheelchair users who
  can self propel up short steep incline or
  are pushed by a fit carer or
  use a power chair and
can stop on a slope to use a door
Sometimes instead of a level platform at doorstep
Notes: <number>
Is sometimes used at doorstep instead of a level platform in conjunction with a regular ramp or lift to reduce the total rise needed for the ramp or lift (in this sitn it would be part of a more complex modification).

## Slide 32: Key points threshold ramps
Gradient is steeper than regular ramp
Maximum length permitted is less than footprint of wheelchair
Unsuitable for threshold step > 56mm
Must have non slip surface
No rails
No kerbs
Notes: <number>
Gradient of regular ramp is 1 in 12.

## Slide 33
Installed – Interior & Exterior Threshold Ramps
Notes: <number>
Inside threshold height was 20mm. Threshold ramp 850mm wide x 100mm long
Outside threshold was 50mm. Threshold ramp was 1000mm wide x 400mm long

## Slide 34: Think about options
Equipment – suppliers in NZ
$$$ -self funding
Complex modification
  regular ramp
  lift
Notes: <number>
Equipment options Suppliers in NZ – Abel Axcess Rob Trubshaw (Wonderful Wedgies), Cubro (rubber & aluminium), Multifit (Excellent Rubber Ramps). Refer to handout
- are portable, can be removed & reissued
Self funding via OT technician or local contractor – inexpensive for ply wedge
Complex mod- may be required depending on individual, environment & expected long term needs

## Slide 35: Determine solution – threshold ramp
Location
Measure height - check <56mm
Design
    width
    length
    splayed
    non slip surface
Construction
    installation
Notes: <number>
Location – which door? Inside plus outside required?
Design - Width- Slightly wider than width of doorway 900-1000mm
- length -<450mm
- splayed side allows approach from different angles, not just front on. May suit if there is a 90’ turn from path to entry
Construction – must be “permanent fixture” installed to property to be considered a housing mod

## Slide 36: DOORWAY WIDENING
Internal doors only
Standard hinged doors with no electrical works
Indicators
    change in mobility aid
    upsize of chair
    change to wheelchair resulting in > footprint
    tight 90’ turn into doorway
Notes: <number>
A hinged door is also known as a side hung door. It hinges on one side and swings in an arc.
No electrical works ie cannot move lightswitch
Indicators –unlikely to be required in isolation from other housing mods unless there has been a change in mobility aid (eg from stick to walker or from walker to wheelchair), upsize of wheelchair due to growth or increase in weight, change in wheelchair need eg move from std wheelchair to wheelchair with a longer wheelbase (TNS, elev legrests).
Is most likely to be needed when the doorway is 90’ from a narrow hallway as a wider space is needed for a turning chair. A wider doorway allows an angled approach to door

## Slide 37: NZ Standards for doorways
Minimum clear width of a doorway shall be 760mm when the door is open
Can be achieved with an 810mm sidehung door
Notes: <number>

## Slide 38: Key points for doorways
Reach. Grasp.Twist. Pull to open. Back up. Release. Go through. Turn. Reach. Grasp. Twist. Push to close. Turn.
Door sizes
Clear opening
Arc of widened door
Notes: <number>
Reach. Grasp…that’s getting a door open & closed. Issues with the actual opening & closing the door won’t be changed by widening the door. It might actually be more cumbersome.
Door size refers to the actual width of the door itself.
Measure size from side edge to side edge with door open), width of open doorway (door frame to where door can be opened to its maximum).
Existing doors tend to be std sizes depending on age of house – entry doors usually wider than internal doors, living & bedroom usually the same, bathroom & toilet usually narrower eg most older HNZ houses in this region have 810 or 860mm front door, 760 internal doors except for bathroom which is 660mm (with only a 610 opening). Hallways may only be 850 or 960mm.
Clear opening is the open width of the doorway (measure from door frame to where door can be opened to its maximum).
is usually 50mm less than the actual door size.
is always narrower than the actual door width as it is made narrower by the thickness of the door itself when it stands wide open plus any other structures behind the door (door handle, door stop 0 which prevent it opening further
Arc of widened door – as the door is widened so too does the swing arc. This may encroach on useable space in the room esp toilet (allow space for users feet when sitting on the toilet.)
Can use a piece of string the same length as proposed door to check this.

## Slide 39: also…for doorways
Hallway width related to doorway width
Approach to door from room
(Homes without Barriers…a guide to accessible houses. BRANZ 2001)
Notes: <number>
Hallway width affects circulation space, room to manoeuvre 90’ through a doorway.
The narrower the hallway the wider the doorway 90’ from the hallway will need to be.
Refer NZS: hall 900 > doorway 1200; hall 1000 >doorway 1000; hall 1200>doorway 760mm.
Approach to door from room A clear space of 300mm between the opening edge of the door & the adjacent wall will make it easier to open the door from a wheelchair.

## Slide 40: Think about options
Technique for manoeuvring
Remove rims from wheelchair
Use shower commode chair for bathroom
Power wheelchair options
Remove door
Rehang door
Fold back hinges
Notes: <number>
Technique for manoeuvring chair through doorway – eg hands off rims & pull self through on dpprframe, remove footplates to reduce overall length
Wheelchair rims – can narrow chair by 50mm
Shower commode chair is narrower than std wheelchair & easier to get thru doorway
Power wheelchairs –MWD more manoeuvrable and can turn in smaller space than RWD
Remove door altogether – “open plan” ok for living areas. Can use heavy curtain for bedroom or bathroom
Rehang door – to swing opposite way. This may allow more space on the opening side which makes it easier to approach on an angle. May be helpful in bathroom where door swings open against bath.
- to swing outwards instead of inwards
Fold back hinges (hospital hinges) replace conventional hinges to allow door to open to the full width of the door frame so it does not protrude into doorway.
will widen doorway opening by width of the door ie by 50mm. Only possible if there is room for door to go back further (not possible if bath is right behind door)

## Slide 41: Determine solution – doorway widening
Location – internal only
Position in relation to space available
Size required (bigger is not necessarily better)
Handles & locks
Door construction
Notes: <number>
Location – which doors are essential
Position – which side of the door to widen? (hinge side or opening side)
Note position of light switches to avoid electrical work
Std sizes start at 610mm & increase in 50mm ie 610mm, 660mm, 710mm, 760mm, 810mm, 860mm, 910mm.
Side hung doors can be made >910mm and also sizes in between the std sizes but they will be a “special” and more expensive.
Choose size depending on – person & their overall width in wheelchair
- difficulty of the manoeuvre
- useability of door (bigger is not necessarily better)
- sizes available as above
Handles & locks- consider ease of operation.
- lever handles easier as push down & pull or push cf knob handles which require grip & twist.
- lever handles with ends returned tow door improve grip & help hand slipping off handle
- oblong handle shape easier to hold than circular
- height 1000mm
- lock type – specify type if impt
Door construction – new door likely to be hollow core door painted white - may not match old doors as door removed may have been solid timber. Client may wish to pay the difference in cost to have matching doors.

## Slide 42: LEVER TAPS

## Slide 43: Key points lever taps
Indicators
Methven range (see handout)
Think about options
    Ensure taps are functioning well
    Equipment - tap turners
Notes: <number>
Indicators – living alone, unable to use existing taps & unable to use tap turners
- joint protection
- pain
Methven – Futura basin mixer for bathroom FT 2050
- Futura sink mixer for kitchen has longer spout

## Slide 44: Funding options basic modifications
Self funding
HNZ
Other organisations eg Veterans Affairs
WINZ
LTSCHC via NASC
EMS funding
Notes: <number>
Options - encourage self funding. Be proactive with supplying families with information to do the job themselves. Provide names of reliable contractors and estimate of price.
HNZ may fund if client is not eligible for EMS funding eg if less than $200 or already has rail at one entrance
Other organisations such as Veterans Affairs
WINZ – may provide a loan
Long term supports chronic health conditions via NASC (prev known as IFP funding) for <65yrs with chronic health conditions & high needs. For those who who do not fir EMS funding criteria.
EMS funding is an option not an automatic. Ensure all eligibity criteria are met

## Slide 45: Sketching is for…
the therapist
the client
the MoH provider
the contractor
…so it’s worth getting it right!
Notes: <number>
For the therapist To help complete the assessment, to help you to work out if what you are proposing is even possible, as a record in the client’s notes, for peer review if needed.
For the client To show client what you are proposing
For the MoH provider as part of an EMS application
For the contractor so he understands what is required & can quote accurately

## Slide 46: Take….
measurements
time to sketch carefully
a photo…if it helps you to remember
Notes: <number>
Measurements –in mm eg 180mm not 18cm. For external rails & threshold ramps note height, width, depth of steps (check within “norm”?)
Sketch – freehand but accurate – contractor will need to quote on sketch as won’t do onsite visit for small job.
- birds eye view and /or side on view
Photo – with client’s permission.

## Slide 47: Helpful hints
How to measure height of steps
How to measure length of step rail
Use pencil & different coloured pens
Use templates for steps, bathrooms
Use grid paper & scale wheelchair
Notes: <number>
Hot tip 1 – place hard covered book (diary) across top edge of step to get accurate 90’ measurement from tread of one step to tread of the next step. Check total height = sum of parts
Hot tip 2 – measure along top edge of steps (pitchline) then add 300 min at top + 300min at bottom
Hot tip 3 - use pencil in rain. Use 2 coloured pens – one for lines & one for measurements
Hot tip 4– use templates for drawing rails (we have some of steps, toilets, baths)
Hot tip 5 – use grid paper & model of wheelchair to same scale to see whether chair can manoeuvre through doors & turn 90’

## Slide 48: Sketching practice
Next….
Translate what you can see into a birds eye view & a side on view
Freehand draw existing & proposed on the same sketch
Notes: <number>
See worksheets

## Slide 49
Worksheet – Sketching Practice
Birds Eye – Proposed Galv Pipe Rail
Side On
Side On
Front on – Proposed Toilet Rail
Notes: <number>
Top photo – 1st step 185 mm, 2nd step 140mm, doorstep 120mm. Step tread is 280mm. Porch 980mm x 740mm.
Bottom photo – toilet – total width of room 950mm. Basin & roll holder on RHS. Studs are 36” in from far corner on both walls. Requires rail on LHS.

## Slide 50
Worksheet – Sketching Practice
Side On
Birds Eye – Existing Doorway & Hall
Birds Eye – Proposed Banister Rail
Proposed Wider Doorway
Notes: <number>
Top photo internal staircase narrow stairs only 740mm wide. Risers uniform 170mm, treads 270mm. Requires bannister rail LHS asc
Bottom photo – doorway at end of hall is 710mm with open width of 660mm. To be widened.

## Slide 51
Side On
Birds Eye – Proposed Threshold Ramps
Worksheet – Sketching Practice
Notes: <number>
Front entry – doorway 860 wide, entry way 1200 wide. Porch 1200 deep. Doorstep 30mm high. Second step to courtyard is 55mm high. Requires threshold ramps x2.

## Slide 52: Resources
Information sheets for EMS assessors
  Rails,steps,easy steps & stairs
  Ramps
  Doors, doorways,walls http://disabilityservices.hiirc.org.nz
NZS 4121: 2001 Design for Access & Mobility – Buildings & Associated Facilities
“More Accessible Housing for Independent Living” Rod A. Hunter 1992
Homes without Barriers…a guide to accessible houses. BRANZ 2001
Grab rails information sheet. SA Disability Information service www.disability.sa.gov.au

## Slide 53: Nail that Rail!…all you need to know to to become an ‘approved assessor' for basic housing modifications
Presented by Angela Vanderpoel
Community Occupational Therapist
28.09.10
15.11.10